## Slide 1: Closed-Form Diffraction Modeling
Terry Bartlett, Zach Walker

## Slide 2: Optical Modeling of DMD Diffraction
Ray tracing is not adequate for diffraction efficiency or contrast modeling
Generally scalar diffraction theory can be used for calculating diffraction efficiency
  Relatively simple DMD model consisting of mirrors only
  Incoherently integrate over wavelength and source extent
  Reference: “Linear systems formulation of non-paraxial scalar diffraction theory” James E. Harvey, Proc. of SPIE Vol. 8122
Contrast modeling is much more complicated requiring more rigorous electromagnetic modeling (will not be covered here)
  Requires very detailed models of pixel structure including dark thin film coatings and CMOS layout
  Finite Difference Time Domain (FDTD) slices very complex 3D geometry into cells and rigorously solves Maxwell’s equations in time

## Slide 3: DMD Behaves Similar to a Blazed Diffraction Grating
0 order
M = +2
+1
D
-1
normal
-2
Direction of reflected light at each diffraction order, m, given by the grating equation
where D is the pitch
Direction/separation of diffraction orders varies with mirror pitch and wavelength
Diffraction orders are fixed and do not separate/spread with mirror tilt
As wavelength increases, so does separation between diffraction orders

## Slide 4: Blaze Condition
0 order
N
N-1
D
N+1
D
N
N-1
N+1
0 order
Blaze condition:
Nearly all energy in one
diffraction order
Off-blaze condition:
Energy spread between
multiple orders
Tilt angle 1
Tilt angle 2
Envelope determined
by pixel mirror shape
and tilt angle

## Slide 5
Diffraction Modeling of Broadband Extended Sources
wavelengths
Pupil positions
Display
screen
Large number of plane waves launched from
multiple directions within illumination pupil
Projection lens
aperture removes
energy outside of
F/number cone
Diffraction model calculates far-field
for each incident plane wave
Integrate fields
incoherently over
wavelength and
position

## Slide 6: DMD diffraction can be treated as a surface scatterer with Bidirectional Scatter Distribution Function (BSDF)
Typical scattering surfaces (isotropic) can be characterized by in-plane BSDF because scattering properties do not change with angle phi. DMD diffraction is discrete and BSDF functions are typically described by continuous functions.
The DMD does NOT behave like this since the scattering properties change with phi.
In spite of this we can use Harvey’s non-paraxial diffraction theory model to describe scatter from the DMD.

## Slide 7: Geometry
Far Field
(direction cosine space)
Discrete diffraction
orders (m,n)
Envelope
determined
by mirror shape
order (3,1)
2=1
Fractional power in each order is
Mirror normal
direction
Incident ray
(plane wave)
direction

## Slide 8: Coordinate System
Spherical Coordinate System
= 12º
= 24º
= 34º
= 17º
= -45º
= -90º

## Slide 9: Coordinate System-Torsional
Illumination
Illumination
Incoming Light
Off-State Light
Hinge Axis
ON
FLAT
OFF
Pupil Diagrams
Mirror On State
θ = 12⁰, Φ = -45⁰
Illumination
θ = 24⁰, Φ = -45⁰
Mirror Off State
θ = -12⁰, Φ = -45⁰
Illumination
θ = 24⁰, Φ = -45⁰

## Slide 10: Coordinate System – Cantilever Design - TRP
Illumination
Illumination
OFF
Off-State Light
Incoming Light
Tilt
Roll
ON
FLAT
Pupil Diagram
Mirror On State
θ = 17⁰, Φ = -90⁰
Illumination
θ = 34⁰, Φ = -90⁰
Mirror Off State
θ = -17⁰, Φ = -90⁰
Illumination
θ = 34⁰, Φ = -90⁰

## Slide 11: Start with Non-Paraxial Scalar Diffraction Theory
Reference:
“Linear systems formulation of non-paraxial scalar diffraction theory”
James E. Harvey, Proc. of SPIE Vol. 8122

## Slide 12: Closed-Form Diffraction Equations (on state)
For each output diffraction order (m, n), an output ray (plane wave)
appears at these direction cosine directions:
2<1
are output ray dir. cosines
where:
are input ray dir. cosines
are mirror normal dir. cosines
are
the mirror pitch
are the
mirror widths
are the integer
diffraction orders
These diffraction orders only exist within the unit circle:

## Slide 13: Closed-Form Diffraction Equations (on state): Reflected ray direction
where:
-2()=(-2ac, -2)
Note that a mirror with normal (-z) illumination and normal
direction cosines a, b will have reflected direction cosines of 2ca and 2cb!

## Slide 14: Closed-Form Diffraction Equations (on state): Large Tilt Angle Correction Term
For
and
where:
are input ray dir. cosines
are mirror normal dir. cosines
are the
mirror pitch
are the
mirror width
are the integer
diffraction orders
and
2<1:
Else:
are output ray dir. cosines

## Slide 15: Diffraction Efficiency Obtained by Summing
For each wavelength the diffraction efficiency within the F/number is given by:
Where:

## Slide 16: TRP or non-TRP?
 | TRP | Non-TRP
 | 17 | 12
 | 0 | 45
 | TRP | Non-TRP
 | 17 | 12
 | 0 | 45
are mirror normal dir. cosines
Mirror normal
direction
=sin()cos()
=sin()sin()